## Slide 1: Re-Examination of Visions for Tokamak Power Plants – The ARIES-ACT Study
Farrokh Najmabadi
Professor of Electrical & Computer Engineering
Director, Center for Energy Research
UC San Diego
and the ARIES Team
TOFE 2012
August 30, 2012

## Slide 2: ARIES Program Participants
Systems code: UC San Diego, PPPL
Plasma Physics: PPPL , GA, LLNL
Fusion Core Design & Analysis: UC San Diego, FNT Consulting
Nuclear Analysis: UW-Madison
Plasma Facing Components (Design & Analysis): UC San Diego, UW-Madison
Plasma Facing Components (experiments): Georgia Tech
Design Integration: UC San Diego, Boeing
Safety: INEL
Contact to Material Community: ORNL

## Slide 3: Goals of ARIES ACT Study
Over a decade since last tokamak study : ARIES-1 (1990) through ARIES-AT(2000).
  Substantial progress in understanding in many areas.
  New issues have emerged: e.g., edge plasma physics, PMI, PFCs, and off-normal events.
    What would be the maximum fluxes that can be handled by in-vessel components in a power plant?
    What level of off-normal events are acceptable in a commercial power plant?
Evolving needs in the ITER and FNSF/Demo era:
  Risk/benefit analysis among extrapolation and attractiveness.
  Detailed component designs is necessary to understand R&D requirements.

## Slide 4: Frame the “parameter space for attractive power plants” by considering the “four corners” of parameter space
Reversed-shear
(βN=0.04-0.06)
DCLL blanket
Reversed-shear
(βN=0.04-0.06)
SiC blanket
1st Stability
(no-wall limit)
DCLL blanket
1st Stability
(no-wall limit)
SiC blanket
ARIES-RS/AT
SSTR-2
EU Model-D
ARIES-1
SSTR
Lower thermal efficiency
Higher Fusion/plasma power
Higher P/R
Metallic first wall/blanket
Higher thermal efficiency
Lower fusion/plasma power
Lower P/R
Composite first wall/blanket
Higher power density
Higher density
Lower current-drive power
Lower power density
Lower density
Higher CD power
Decreasing P/R
Physics Extrapolation
ACT-1
Engineering performance (efficiency)

## Slide 5: Status of the ARIES ACT Study
Project Goals:
  Detailed design of advanced physics, SiC blanket ACT-1 (ARIES-AT update).
  Detailed design of ACT-2 (conservative physics, DCLL blanket).
  System-level definitions for ACT-3 & ACT-4.
ACT-1 research will be completed by Dec. 2012.
  First design iteration was completed for a 5.5 m Device.
  Updated design point at R = 6.25 m (detailed design on-going)
  9 papers in this conference.
ACT-2 Research will be completed by June 2013.

## Slide 6: ARIES-ACT1 (ARIES-AT update)
Advance tokamak mode
Blanket: SiC structure & LiPb Coolant/breeder (to achieve a high efficiency)

## Slide 7: ARIES Systems Code – a new approach to finding operating points
Systems codes find a single operating point through a minimization of a figure of merit with certain constraints
  Very difficult to see sensitivity to assumptions.
Our new approach to systems analysis is based on surveying the design space and finding a large number of viable operating points.
A GUI is developed to visualize the data. It can impose additional constraints to explore sensitivities
Example: Data base of operating points with
fbs ≤ 0.90, 0.85 ≤ fGW ≤ 1.0, H98 ≤ 1.75

## Slide 8: Impact of the Divertor Heat load
Divertor design can handle > 10 MW/m2 peak load.
UEDGE simulations (LLNL) showed detached divertor solution to reach high radiated powers in the divertor slot and a low peak heat flux on the divertor (~5MW/m2 peak).
  Leads to ARIES-AT-size device at R=5.5m.
  Control & sustaining a detached divertor?
Using Fundamenski SOL estimates and 90% radiation in SOL+divertor leads to a 6.25-m device with only 4 mills cost penalty (current reference point).
  Device size is set by the divertor heat flux

## Slide 9: The new systems approach underlines robustness of the design point to physics achievements
Major radius (m) | 6.25 | 6.25
Aspect ratio | 4 | 4
Toroidal field on axis (T) | 6 | 7
Peak field on the coil (T) | 11.8 | 12.9
Normalized beta* | 5.75% | 4.75%
Plasma current (MA) | 10.9 | 10.9
H98 | 1.65 | 1.58
Fusion power (MW) | 1813 | 1817
Auxiliary power | 154 | 169
Average n wall load (MW/m2) | 2.3 | 2.3
Peak divertor heat flux (MW/m2) | 10.6 | 11.0
Cost of Electricity (mills/kWh) | 67.2 | 68.9
* Includes fast a contribution of ~ 1%

## Slide 10: The new systems approach underlines robustness of the design point to physics achievements
Major radius (m) | 6.25 | 6.25
Aspect ratio | 4 | 4
Toroidal field on axis (T) | 6 | 7
Peak field on the coil (T) | 11.8 | 12.9
Normalized beta* | 5.75% | 4.75%
Plasma current (MA) | 10.9 | 10.9
H98 | 1.65 | 1.58
Fusion power (MW) | 1813 | 1817
Auxiliary power | 154 | 169
Average n wall load (MW/m2) | 2.3 | 2.3
Peak divertor heat flux (MW/m2) | 10.6 | 11.0
Cost of Electricity (mills/kWh) | 67.2 | 68.9
* Includes fast a contribution of ~ 1%

## Slide 11: Detailed Physics analysis has been performed using the latest tools
New physics modeling
  Energy transport assessment: what is required and model predictions
  Pedestal treatment
  Time-dependent free boundary simulations of formation and operating point
  Edge plasma simulation (consistent divertor/edge, detachment, etc)
  Divertor/FW heat loading from experimental tokamaks for transient and off-normal*
  Disruption simulations*
  Fast particle MHD
* Discussed in the paper by C. Kessel, this session

## Slide 12: Overview of engineering design: 1. High-hest flux components*
Design of first wall and divertor options
  High-performance He-cooled W-alloy divertor, external transition to steel
  Robust FW concept (embedded W pins)
Analysis of first wall and divertor options
  Birth-to-death modeling
  Yield, creep, fracture mechanics
  Failure modes
Helium heat transfer experiments
ELM and disruption loading responses
  Thermal, mechanical, EM & ferromagnetic
* Discussed in papers by M. Tillack and J. Blanchard, this session

## Slide 13: Overview of engineering design*: 2. Fusion Core
Features similar to ARIES-AT
  PbLi self-cooled SiC/SiC breeding blanket with simple double-pipe construction
  Brayton cycle with h~60%
Many new features and improvements
  He-cooled ferritic steel structural ring/shield
  Detailed flow paths and manifolding for PbLi to reduce 3D MHD effects**
  Elimination of water from the vacuum vessel, separation of vessel and shield
  Identification of new material for the vacuum vessel***
* Discussed in the paper by M. Tillack, this session
** Discussed in the paper by X. Wang, this session
*** Discussed in the paper by L. El_Guebaly, this session

## Slide 14: Detailed safety analysis has highlighted impact of tritium absorption and transport
Detailed safety modeling of ARIES-AT (Petti et al) and ARIES-CS (Merrill et al, FS&T, 54, 2008 ) have shown a paradigm shift in safety issues:
  Use of low-activation material and care design has limited temperature excursions and mobilization of radioactivity during accidents. Rather off-site dose is dominated by tritium.
  For ARIES-CS worst-case accident, tritium release dose is 8.5 mSv (no-evacuation limit is 10 mSV)
Major implications for material and component R&D:
  Need to minimize tritium inventory (control of breeding, absorption and inventory in different material)
  Design implications: material choices, in-vessel components, vacuum vessel, etc.

## Slide 15: In summary …
ARIES-ACT study is re-examining the tokamak power plant space to understand risk and trade-offs of higher physics and engineering performance with special emphais on PMI/PFC and off-normal events.
  ARIES-ACT1 (updated ARIES-AT) is near completion.
  Detailed physics analysis with modern computational tools are used. Many new physics issues are included.
  The new system approach indicate a robust design window for this class of power plants.
  Many engineering imporvements: He-cooled ferritic steel structural ring/shield, Detailed flow paths and manifolding to reduce 3D MHD effects, Identification of new material for the vacuum vessel …
  In-elastic analysis of component including Birth-to-death modeling and fracture mechanics indicate a higher performance PFCs are possible. Many issues/properties for material development & optimization are identified.

## Slide 16: Thank you!